## Slide 1
What a solution looks like
Instance RshortCfewTmedium_19 (899 km, 14 charging stations, 28 rest areas, 1 customer)
RO plan, executed as-is • depart 08:00, arrive 08:52 next day (24.9 h) • feasible under realised travel times, customer window met
Route
197 km
224 km
418 km
554 km
725 km
O
0 km
D
899 km
C1
Rest area
Charging station
Customer
Stop used by the solution
Charge & 15 min break
(1st split, gi = τic)
Service + 30 min break
(2nd split)
Charge, then 9 h rest
(sequential: σi = 1, gi = 0)
Charge & 45 min break
(gi = τic)
Charge & 45 min break
Mistop
Qi
τic
Miseq
Truck
Driving
Driving
Driving
Driving
Driving
truck parked (τir)
SOC
[kWh]
Ecap
Emin
100
300
500
midnight
HoS
[h]
4.5 h
9 h
0
4.5
9
consecutive driving tdrv
shift driving tsd
08:00
10:00
12:00
14:00
16:00
18:00
20:00
22:00
00:00
02:00
04:00
06:00
08:00
Driver
Driving
Driving
Driving
Driving
Driving
Working time
1st split break (15′)
Service
2nd split break (30′)
Working time
9 h rest (reduced)
Working time
45′ break
Working time
45′ break
run RshortCfewTmedium_19_RO_20260716_092310_060 • break rules: 45′ after ≤ 4.5 h driving, splittable 15′+30′; daily rest 11 h (9 h reduced) • charge counts as break when concurrent (gi), as work when followed by rest (σi = 1)